## Slide 1: AWCI session, 12th AOGEO Symposium, 3/11/2019, Canberra, australia [National report] platform on Water resilience and disasters in the Philippines
Mr. Michael T. Alpasan, DPWH
Mr. Socrates F. Paat Jr., DOST-PAGASA
Mr. Jonathan P. Victolero, DOST XI
Dr. Patricia Ann J. Sanchez, University of the Philippines Los Banos

## Slide 2: National report on the platform activity
1st Plenary Meeting Concept sharing
13/3/2017, Metro Manila Platform formulation
2nd Plenary Meeting Data sharing guideline
15/6/2017, Metro Manila Data list creation
Representative Meeting Data list confirmation
18/9/2017, Hanoi
Individual Meeting Secretariat assignment
7-9/2/2018, Metro Manila Data collection
Individual Meeting Secretariat assignment
12-13/3/2018, Metro Manila HLPW outcome document
Stakeholders Meeting Data upload
18/5/2018, Davao
11th GEOSS Symposium Regional coordination
24-26/10/2018, Kyoto
3rd Plenary Meeting Activity update
7/2/2019, Metro Manila implementation
Category 1:
Full open
Category 2:
Among Platform
Category 3:
With permission
Concept of Platform
Data Sharing Guideline
Progress of Platform Activity
Michael-san

## Slide 3: National report on the platform activity
The 3rd Plenary Meeting of Platform
Agency | Office/Division
DPWH | UPMO-FCMC
 | Regional Office III
 | Regional Office XI
DOST | PAGASA
 | PHIVOLCS
 | PCIEERD
 | Regional Office II
 | Regional Office III
 | Regional Office XI
DENR | NAMRIA
 | Regional Office XI
DILG | WSSPMO-OPDS
DND | OCD
 | Regional Office XI
DSWD | 
LGA | 
MGB | 
NEDA | Regional Office III
 | Regional Office XI
NWRB | 
PSA | 
NIA | 
UP Los Banos | 
UP Diliman | 
UP Mindanao | 
Univ. of Tokyo | EDITORIA
ICHARM | 
Typhoon Committee | 
78 participants from 28 offices
Michael-san

## Slide 4: National report on the platform activity
Institutional Structure
Michael-san

## Slide 5: National report on the platform activity
Activity Plan
Michael-san

## Slide 6: National report on the platform activity
1. Data Integration
Socio-economy
Damage
Hazard
Hydro-met Division
Statistic Authority
Disaster Division
River Bureau
Agricultural Depart.
Space Agency
Economic Authority
Geospatial Authority
Environment Depart.
Trade & Industry Depart.
LGU
Sci. & Tech.
Depart.
Overall
Jonathan-san

## Slide 7: National report on the platform activity
1. Data Integration
Metadata Template
Data | Source of information
Casualties & missing person | OCD
Num. of affected people | OCD
Agricultural damage | DA
Housing damage | OCD
Damage to critical infrastructure | DPWH, LGU
Direct economic loss other than agricultural loss | LGU NEDA
Data | Source of information
DEM (LiDAR) | UP Mindanao
DEM (ifSAR) | NAMRIA
Hydromet data | PAGASA, ASTI, DREAM
Inundation depth (LiDAR) | UP Diliman, UP Mindanao
Inundation depth (interview) | PAGASA
Rainfall | PAGASA
River flow | DPWH, UP Mindanao
River cross section | DPWH, UP Mindanao
Tidal level | NAMRIA
Data | Source of information
Land use | LGU, DOST
Agriculture | PSA, DA
Population | PSA
Infrastructure | DPWH/LGU
Industry | DTI
Commerce | DTI
Drainage facility | DPWH/LGU
Information | PSA, NEDA
Sectoral Regional GDP | PSA
Sectoral employed population | PSA
Tax revenue | BIR
Land price | City Assessors Office
Damage
Hazard
Socioeconomic
Data | Source of information
Casualties & missing person | OCD
Num. of affected people | OCD
Agricultural damage | DA
Housing damage | OCD
Damage to critical infrastructure | DPWH, LGU
Direct economic loss other than agricultural loss | LGU NEDA
Data | Source of information
Land use | LGU, DOST
Agriculture | PSA, DA
Population | PSA
Infrastructure | DPWH/LGU
Industry | DTI
Commerce | DTI
Drainage facility | DPWH/LGU
Information | PSA, NEDA
Sectoral Regional GDP | PSA
Sectoral employed population | PSA
Tax revenue | BIR
Land price | City Assessors Office
Damage
Hazard
Socioeconomic
Data | Source of information
DEM (LiDAR) | UP Mindanao
DEM (ifSAR) | NAMRIA
Hydromet data | PAGASA, ASTI, DREAM
Inundation depth (LiDAR) | UP Diliman, UP Mindanao
Inundation depth (interview) | PAGASA
Rainfall | PAGASA
River flow | DPWH, UP Mindanao
River cross section | DPWH, UP Mindanao
Tidal level | NAMRIA
Collected
Jonathan-san

## Slide 8: National report on the platform activity
1. Web-based Data Uploading System
Input Item;
Data Domain, Area, District :
Category:
Data Source
Data Type
Period
Resolution
Jonathan-san

## Slide 9: National report on the platform activity
2. Flood Forecasting & Early Warning
Pampanga River basin
Catchment Area: 10,434km2
River Length: 260km
Annual Rainfall: 2,155ｍｍ
Rain Gauge: 17 stations
Water Level: 11 stations
Observation
Land use
Flood vulnerability
Jun-san

## Slide 10: National report on the platform activity
2. Flood Forecasting & Early Warning (Model Calibration)
Chart: Sapang Buho Station
SIMULATION_without Panta RR
simulation with PantaRR
simulation1
simulation2
simulation applying the 2012 Rating Equation
simulation using the ground rainfall (2009 RE)
Observed Discharge (2009 Rating Equation)
simulation using the ground rainfall (2009 RE)
modified channel
Simulation (based on 2009 Rating Equation)
Chart: San Isidro Station
SIMULATION_without Panta RR
simulation with PantaRR
simulation1
simulation2
simulation applying the 2012 Rating Equation
simulation using the ground rainfall (2009 RE)
Observed Discharge (2009 Rating Equation)
simulation using the ground rainfall (2009 RE)
modified channel
Simulation (based on 2009 Rating Equation)
NSE= 0.63
NSE= 0.68
MODIS 8days composite
Unit forest crop water
Jun-san

## Slide 11: National report on the platform activity
2. Flood Forecasting & Early Warning (Full Design)
Cloud Image
HIMAWARI-8
In-situ
Gauge
Satellite Rainfall
GSMaP
Satellite Image
ALOS-2
Dam Operation
Inundation extent
Inundation depth
River discharge
RRI Model
Simulation
Flood prevention & evacuation
In-situ
Radar
ALOS © JAXA (2016)
Monitoring
Forecasting
Numerical Weather Prediction
Jun-san

## Slide 12: National report on the platform activity
2. Flood Forecasting & Early Warning (Preliminary)
PAGASA
Server
Authorized
Part
Realtime Access
In-situ
Gauge
Satellite Rainfall
GSMaP
Cloud Image
HIMAWARI-8
Jun-san

## Slide 13: National report on the platform activity
3. Climate Change Impact (Pampanga River Basin)
Past climate
Future climate
RCP8.5
Difference (future)-(past)
Annual total
JJA
DJF
Weather Research and Forecasting (WRF) ver.3.4.1
Horizontal resolution: 15km/ 5km
Coordinate: 67×67×40 (outer), 67×67×40 (inner)
Cumulus parameterization: Grell 3D
Microphysics: WSM3class
PBL scheme: MYNN2.5
Surface: Thermal diffusion
Rain gauges
Pampanga River Basin
Seasonal Variation of Rainfall
(a little increase, but not much)
Rainfall distribution in past and future climate
46% increase of 1/50 extreme rainfall ⇒One flood event causes more damage
Jun-san

## Slide 14: National report on the platform activity
3. Climate Change Impact (Davao River Basin)
WRF model setting
Outer frame: 15km, 100x100
Inner frame: 5km, 79x79
Vertical layer: 40
Cumulus: Grell 3D
Δx=5km
Davao River
Area: 1623 km2
Length: 160 km
Past climate
Future climate
RCP8.5
Difference (future)-(past)
Annual total
JJA
DJF
Rainfall distribution in past and future climate
Raingauge
Past Climate
Future Climate (RCP8.5)
Seasonal Variation of Rainfall
(increase during July to September)
33% increase of 1/50 extreme rainfall & July-September rainfall increase 45% ⇒Average discharge increases + one flood event causes more damage
Jun-san

## Slide 15: National report on the platform activity
4. Economic Assessment
Production
（GRP:Gross Regional
Product）
Y
Private Capital Stock
Kp
Labor Force
L
Y=AKpαLβ
Production Function
⊿Y =Yafter－Ybefore =(AKafterα L afterβ )－ (AKbeforeα L beforeβ )
Damage of Depreciable Assets of Offices
Number of Days with business interruption and Delay Death due to disaster
Operational Ratio of Society
Robustness
Resilience
With countermeasures
Without countermeasures
100%
Build Back Better
Emergency Response
Patricia-san

## Slide 16: National report on the platform activity
5. Contingency Planning
2011Typhoon Pedring
Source: OCD-3/PRFFWC
Pampanga River Basin: Catchment Area: 10,434 km2
River Length: 260 km
Average annual rainfall:
2155 mm/year
Calumpit Municipality:
Population: 112,007
Barangay(Local community unit): 29
Households: 22,402
Area: 5,625 ha
Ordinary Flood (10 Years)
High Flood (30 Years)
Extreme Flood (100 Years)
Interferometric Synthetic Aperture Radar (IfSAR) Data provided by NAMRIA, Philippines, was used in the calculation (grid size/ 5m).
Patricia-san

## Slide 17: National report on the platform activity
5. Contingency Planning
Identify the flood hot spots
Google Earth Street View with inundation visualization
(High Flood Case)
Total Score
District-base analysis
Patricia-san

## Slide 18: Proposal of capacity development
CC Orientation
Objective
- Contribution adaptation measures development
- Encouragement and coordination of multi-stakeholder engagement
Expected Output
- Activity design for CC adaptation
- Barangay-level damage data analysis
2. Platform Plenary Meeting
Objective
- Status sharing and update of the Platform activities among all members
- Discussion on further activities of Platform
Expected Output
- FF System for Davao RB
- Data integration examples
3. DIAS End-user Training
Objective
- To capacitate end-users on the know-how of DIAS
- To maximize the utilization of DIAS
Expected Output
- Data uploading by stakeholders
- Data integration products
4. Policy & Benchmarking WS
Objective
- Contribution to local policy-making on CC
- Best practice on the importance, applicability and usability.
Expected Output
- Policy proposal on CC adaptation to Mayor
- Community action
Oct.
2019
Apr.
2020
2020
2020
Workplan of Capacity Development on Climate Change in Davao City
Jonathan-san

## Slide 19: Proposal of capacity development
Activity Design
Toward the Prosperous Davao
Strengthening Resilience
Experiencing Climate Change
Climate change impact assessment based on S&T
Experiencing Events
Infrastructure design
1/100 Flood (200m grid)
Visualization
Predict climate change impact and scenario
Resilient communities
Incentive for investment
Resilient society beyond saving lives
Design a brilliant future
SAFE: S&T Action Frontline for Emergencies and Hazards Program
Coordination with relevant ongoing energies
Be Climate Smart NOW
Agriculture, Aquaculture and Natural Resources (AANR)
biodiversity
Groundwater use
Bright tomorrow of Davao
Attractive policy proposal
Setting All
Evacuation
“Nudging” psychological process to disaster risk
Area BCM;
Business
Continuity
Management
Jonathan-san

## Slide 20: Proposal of capacity development
If any from DPWH
Michael-san

## Slide 21: Proposal of capacity development
If any from PAGASA
Jun-san

## Slide 22: Proposal of capacity development
If any from UPLB, maybe, SATREPS
Patricia-san

## Slide 23: Roadmap/strategic way for global agenda
From each organization, because discussion on roadmap continues to afternoon session.
All of you